## Slide 1: CIS 490H/590J Edge Computing Network Basics
Winter 2023
Prof. Zheng Song
zhesong@umich.edu

## Slide 2: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket
Content Distribution Network (CDN)
Mobile and wireless network
SDN and NFV
Slides adopted from Computer Networking: A Top Down Approach

## Slide 3: The Internet: a “nuts and bolts” view
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Packet switches: forward packets (chunks of data)
  routers, switches
Communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Billions of connected computing devices:
  hosts = end systems
  running network apps at Internet’s “edge”
Networks
  collection of devices, routers, links: managed by an organization

## Slide 4: “Fun” Internet-connected devices
IP picture frame
Web-enabled toaster +
weather forecaster
Internet phones
Internet
refrigerator
Slingbox: remote
control cable TV
Tweet-a-watt:
monitor energy use
sensorized,
bed
mattress
Security Camera
Amazon Echo
Pacemaker & Monitor
Others?
Fitbit
AR devices

## Slide 5: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers

## Slide 6: A closer look at Internet structure
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links

## Slide 7: A closer look at Internet structure
Network edge:
hosts: clients and servers
servers often in data centers
Access networks, physical media:
wired, wireless communication links
Network core:
  interconnected routers
  network of networks
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 8: The network core
mesh of interconnected routers
packet-switching: hosts break application-layer messages into packets
  forward packets from one router to the next, across links on path from source to destination
  each packet transmitted at full link capacity
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network

## Slide 9: Two key network-core functions
Forwarding:
local action: move arriving packets from router’s input link to appropriate router output link
1
2
3
0111
destination address in arriving
packet’s header
routing algorit
header value
output link
0100
0101
0111
1001
3
2
2
1
Routing:
global action: determine source-destination paths taken by packets
routing algorithms
local forwarding table
local forwarding table
routing algorithm

## Slide 10: Internet structure: a “network of networks”
Tier 1 ISP
Tier 1 ISP
Regional ISP
Regional ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
access
ISP
IXP
IXP
IXP
At “center”: small # of well-connected large networks
  “tier-1” commercial ISPs (e.g., Level 3, Sprint, AT&T, NTT), national & international coverage
  content provider networks (e.g., Google, Facebook): private network that connects its data centers to Internet, often bypassing tier-1, regional ISPs
Google

## Slide 11: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN

## Slide 12: How do packet loss and delay occur?
packets queue in router buffers
packets queue, wait for turn
arrival rate to link (temporarily) exceeds output link capacity: packet loss
A
B
packet being transmitted (transmission delay)
packets in buffers (queueing delay)
free (available) buffers: arriving packets
dropped (loss) if no free buffers

## Slide 13: Packet delay: four sources
dproc: processing
check bit errors
determine output link
typically < msec
dqueue: queueing delay
time waiting at output link for transmission
depends on congestion level of router
propagation
processing
queueing
Delay = dproc + dqueue + dtrans + dprop
A
B
transmission

## Slide 14: Packet delay: four sources
propagation
processing
queueing
d = dproc + dqueue + dtrans + dprop
A
B
transmission
dtrans: transmission delay:
L: packet length (bits)
R: link transmission rate (bps)
dtrans = L/R
dprop: propagation delay:
d: length of physical link
s: propagation speed (~2x108 m/sec)
dprop = d/s
dtrans and dprop
very different

## Slide 15: How to reduce Latency?
Reduce the number of hops (processing delay)
Reduce the distance from sender to receiver (propagation delay)
Better network interfaces (reduce transmission delay)
No congestion (queue delay)

## Slide 16: Real Internet delays and routes
1 cs-gw (128.119.240.254) 1 ms 1 ms 2 ms
2 border1-rt-fa5-1-0.gw.umass.edu (128.119.3.145) 1 ms 1 ms 2 ms
3 cht-vbns.gw.umass.edu (128.119.3.130) 6 ms 5 ms 5 ms
4 jn1-at1-0-0-19.wor.vbns.net (204.147.132.129) 16 ms 11 ms 13 ms
5 jn1-so7-0-0-0.wae.vbns.net (204.147.136.136) 21 ms 18 ms 18 ms
6 abilene-vbns.abilene.ucaid.edu (198.32.11.9) 22 ms 18 ms 22 ms
7 nycm-wash.abilene.ucaid.edu (198.32.8.46) 22 ms 22 ms 22 ms
8 62.40.103.253 (62.40.103.253) 104 ms 109 ms 106 ms
9 de2-1.de1.de.geant.net (62.40.96.129) 109 ms 102 ms 104 ms
10 de.fr1.fr.geant.net (62.40.96.50) 113 ms 121 ms 114 ms
11 renater-gw.fr1.fr.geant.net (62.40.103.54) 112 ms 114 ms 112 ms
12 nio-n2.cssi.renater.fr (193.51.206.13) 111 ms 114 ms 116 ms
13 nice.cssi.renater.fr (195.220.98.102) 123 ms 125 ms 124 ms
14 r3t2-nice.cssi.renater.fr (195.220.98.110) 126 ms 126 ms 124 ms
15 eurecom-valbonne.r3t2.ft.net (193.48.50.54) 135 ms 128 ms 133 ms
16 194.214.211.25 (194.214.211.25) 126 ms 128 ms 126 ms
17 * * *
18 * * *
19 fantasia.eurecom.fr (193.55.113.142) 132 ms 128 ms 136 ms
traceroute: gaia.cs.umass.edu to www.eurecom.fr
3 delay measurements from
gaia.cs.umass.edu to cs-gw.cs.umass.edu
* means no response (probe lost, router not replying)
trans-oceanic link
* Do some traceroutes from exotic countries at www.traceroute.org
looks like delays decrease! Why?
3 delay measurements
to border1-rt-fa5-1-0.gw.umass.edu

## Slide 17: Throughput
throughput: rate (bits/time unit) at which bits are being sent from sender to receiver
  instantaneous: rate at given point in time
  average: rate over longer period of time
server, with
file of F bits
to send to client
link capacity
Rs bits/sec
link capacity
Rc bits/sec
server sends bits
(fluid) into pipe
pipe that can carry
fluid at rate
(Rs bits/sec)
pipe that can carry
fluid at rate
(Rc bits/sec)

## Slide 18: Throughput
Rs < Rc What is average end-end throughput?
Rs bits/sec
Rc bits/sec
Rs > Rc What is average end-end throughput?
link on end-end path that constrains end-end throughput
bottleneck link
Rs bits/sec
Rc bits/sec

## Slide 19: Where is the bottleneck link?
The link to Data centers?
The link of our access network?
It really depends on how many users are using the same link.
10 users sharing 1Gbps (access network)
10K users sharing 1000Gbps (data center network)
Which is more likely to suffer from congestion?

## Slide 20: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN

## Slide 21: Some network apps
social networking
Web
text messaging
e-mail
multi-user network games
streaming stored video (YouTube, Hulu, Netflix)
P2P file sharing
voice over IP (e.g., Skype)
real-time video conferencing
Internet search
remote login
…

## Slide 22: Client-server paradigm
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
server:
always-on host
permanent IP address
often in data centers, for scaling
clients:
contact, communicate with server
may be intermittently connected
may have dynamic IP addresses
do not communicate directly with each other
examples: HTTP, IMAP, FTP

## Slide 23: Peer-peer architecture
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
no always-on server
arbitrary end systems directly communicate
peers request service from other peers, provide service in return to other peers
  self scalability – new peers bring new service capacity, as well as new service demands
peers are intermittently connected and change IP addresses
  complex management
example: P2P file sharing

## Slide 24: Client-server vs. P2P: example
client upload rate = u, F/u = 1 hour, us = 10u, dmin ≥ us

## Slide 25: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN

## Slide 26: Processes communicating
process: program running within a host
within same host, two processes communicate using inter-process communication (defined by OS)
processes in different hosts communicate by exchanging messages
client process: process that initiates communication
server process: process that waits to be contacted
note: applications with P2P architectures have client processes & server processes
clients, servers

## Slide 27: Sockets
process sends/receives messages to/from its socket
socket analogous to door
  sending process shoves message out door
  sending process relies on transport infrastructure on other side of door to deliver message to socket at receiving process
  two sockets involved: one on each side
Internet
controlled
by OS
controlled by
app developer
transport
application
physical
link
network
process
transport
application
physical
link
network
process
socket

## Slide 28: Addressing processes
to receive messages, process must have identifier
host device has unique 32-bit IP address
Q: does IP address of host on which process runs suffice for identifying the process?
identifier includes both IP address and port numbers associated with process on host.
example port numbers:
  HTTP server: 80
  mail server: 25
to send HTTP message to gaia.cs.umass.edu web server:
  IP address: 128.119.245.12
  port number: 80
more shortly…
  A: no, many processes can be running on same host

## Slide 29: Internet transport protocols services
TCP service:
reliable transport between sending and receiving process
flow control: sender won’t overwhelm receiver
congestion control: throttle sender when network overloaded
does not provide: timing, minimum throughput guarantee, security
connection-oriented: setup required between client and server processes
UDP service:
unreliable data transfer between sending and receiving process
does not provide: reliability, flow control, congestion control, timing, throughput guarantee, security, or connection setup.
Q: why bother? Why is there a UDP?

## Slide 30: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN

## Slide 31: Video Streaming and CDNs: context
stream video traffic: major consumer of Internet bandwidth
  Netflix, YouTube, Amazon Prime: 80% of residential ISP traffic (2020)
challenge:
  scale - how to reach ~1B users?
  Latency - how to avoid lagging

## Slide 32: Content distribution networks (CDNs)
challenge: how to stream content (selected from millions of videos) to hundreds of thousands of simultaneous users?
  enter deep: push CDN servers deep into many access networks
    close to users
    Akamai: 240,000 servers deployed in more than 120 countries (2015)
  bring home: smaller number (10’s) of larger clusters in POPs near (but not within) access networks
    used by Limelight
store/serve multiple copies of videos at multiple geographically distributed sites (CDN)

## Slide 33: Content distribution networks (CDNs)
Notes: 33
Akamai: 100,000+ servers in 1000+ clusters in 1000+ networks in 70+ countries serving trillions of requests a day.
How many people use Netflix?

## Slide 34: CDN use case
netcinema.com
KingCDN.com
1
1. Bob gets URL for video http://netcinema.com/6Y7B23V
from netcinema.com web page
2
2. resolve http://netcinema.com/6Y7B23V
via Bob’s local DNS
netcinema’s
authoratative DNS
3
3. netcinema’s DNS returns CNAME for
http://KingCDN.com/NetC6y&B23V
4
5
6. request video from
KINGCDN server,
streamed via HTTP
KingCDN
authoritative DNS
Bob’s
local DNS
server
Bob (client) requests video http://netcinema.com/6Y7B23V
video stored in CDN at http://KingCDN.com/NetC6y&B23V

## Slide 35: Amazon CDN: Cloudfront
100 points in 2017, 200 points in 2019.
New generation of CDN: not just storage, but also computing
https://aws.amazon.com/blogs/networking-and-content-delivery/how-to-accelerate-your-wordpress-site-with-amazon-cloudfront/
Edge locations: Washington, DC (11); Chicago, IL (19); New York, NY (10); Atlanta, GA (10); Los Angeles, CA (9); Miami, FL (11); Dallas-Fort Worth, TX (11); Houston, TX (4); San Francisco, CA (6); Boston, MA (5); Denver, CO (3); Portland, OR (2); Seattle, WA (6); Toronto, Canada (3); Minneapolis, MN (4); Phoenix, AZ (2); Querétaro, Mexico (2); Montréal, Canada (2); Philadelphia, PA (1); Salt Lake City, UT (1); Vancouver, Canada (1); Nashville, TN (2); Detroit, MI (2)

## Slide 36: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN

## Slide 37: Wireless and Mobile Networks: context
M2M
Smart meters
E-readers
Medical devices
Automobiles
Office devices
Military devices…
Internet of everything (Cisco)
Smarter Planet (IBM)
Notes: machine-to-machine (M2M) connections that support IoT applications will account for more than half of the world's 27.1 billion devices and connections.

## Slide 38: Wireless and Mobile Networks: context
Most devices/access networks go wireless!
WPAN
WLAN
LPWA (LoRa)
Cellular
5G
…
WPAN: Wireless Personal Area Network
WLAN: Wireless Local Area Network
LPWA: low power wide area network
Notes: LPWA, low power wide area network. (Lora）

## Slide 39: Outline
Wireless Communication characteristics
Different Wireless Communication technologies
WiFi: 802.11 wireless LANs
Cellular networks: 4G and 5G
Personal Area Network: BLE, Zigbee, …
LPWA: LoRa
Wireless Sensor Network
Mesh WSN
Delay Tolerant Network
VANET

## Slide 40: Elements of a wireless network
wired network
infrastructure

## Slide 41: Elements of a wireless network
wired network
infrastructure
wireless hosts
laptop, smartphone, IoT
run applications
may be stationary (non-mobile) or mobile
  wireless does not always mean mobility!

## Slide 42: Elements of a wireless network
wired network
infrastructure
base station
typically connected to wired network
relay - responsible for sending packets between wired network and wireless host(s) in its “area”
  e.g., cell towers, 802.11 access points

## Slide 43: Elements of a wireless network
wired network
infrastructure
wireless link
typically used to connect mobile(s) to base station, also used as backbone link
multiple access protocol coordinates link access
various transmission rates and distances, frequency bands

## Slide 44: Characteristics of selected wireless links
Indoor
Outdoor
Midrange
outdoor
Long range
outdoor
10-30m
50-200m
200m-4Km
4Km-15Km
2 Mbps
4G LTE
802.11ac
802.11n
802.11g
802.11b
3.5 Gbps
600 Mbps
54 Mbps
11 Mbps
Bluetooth
802.11ax
14 Gbps
5G
10 Gbps
802.11 af,ah
Hidden: Energy Consumption/Deployment Cost

## Slide 45: Elements of a wireless network
wired network
infrastructure
infrastructure mode
base station connects mobiles into wired network
handoff: mobile changes base station providing connection into wired network

## Slide 46: Elements of a wireless network
ad hoc mode
no base stations
nodes can only transmit to other nodes within link coverage
nodes organize themselves into a network: route among themselves

## Slide 47: Wireless network taxonomy
single hop
multiple hops
infrastructure
(e.g., APs)
no
infrastructure
host connects to base station (WiFi, cellular) which connects to larger Internet
no base station, no connection to larger Internet (Bluetooth, ad hoc nets)
host may have to relay through several wireless nodes to connect to larger
Internet: mesh net
no base station, no connection to larger Internet. May have to relay to reach other a given wireless node MANET, VANET

## Slide 48: 4G/5G Network
4G Focus Area
5G Focus Area
Data
Speed/Throughput
Connection Density
Latency/Delay

## Slide 49: Why we need 5G?
Andrea Goldsmith, What’s Beyond 5Ghttps://www.youtube.com/watch?v=ReGofBrbuLU
https://www.youtube.com/watch?v=GEx_d0SjvS0

## Slide 50: Outline
Network Edge and Core
Network Performance measurement
Network Application Architecture: C/S vs. P2P
TCP/UDP & Socket Programming
Content Distribution Network (CDN)
Mobile and wireless network
SDN/NFV

## Slide 51: Software Defined Network
Write a program to control the network’s behavior

## Slide 52: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane to computer forwarding tables
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 53: Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized “flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
routing
access control
load
balance
4. programmable control applications

## Slide 54: Network Function Virtualization
Network functions virtualization (NFV) is the replacement of network appliance hardware with virtual machines. The virtual machines use a hypervisor to run networking software and processes such as routing and load balancing.
While NFV separates networking services from dedicated hardware appliances, software-defined networking, or SDN, separates the network control functions such as routing,

## Slide 55: ETSI: 5G network
Key enablers:
  Communication end: MIMO, Beamforming
  MEC (Edge/Fog Computing)
  SDN, NFV
  MEC: Mobile Edge Computing provides an IT service environment and cloud-computing capabilities at the edge of the mobile network