## Slide 1: CIS 490H/590J Edge Computing Multi-Layer Computing: End Devices
Winter 2022
Prof. Zheng Song
zhesong@umich.edu

## Slide 2: Outline
End Devices (data producers):
  Common features
  Raspberry Pi, Arduino, ESP32, Jetson TX2 NX
  mobile devices
  Vehicle as a mobile sensor
IoT Gateway
IoT Communication Protocols
  BLE, Zigbee
  MQTT, coAP, websocket
IoT applications:
  indoor localization
  Personal sensing
  crowdsensing
  wireless sensor network

## Slide 3: IoT devices
Less powerful than computers
Embedded operating systems (or without OS)
Equipped with more wireless communication modules
  WiFi, BLE, Cellular
  RFID, Zigbee, Lora (long range, low rate)
Work with Sensors and controllers
Heterogeneity
Some powered by battery
  Sensitive to energy efficiency
  Low energy consumption (3~15W)
    PC: 60~300 Watts
    Laptop: 20~100 Watts
    Server: 500 ~ 1200 Watts

## Slide 4: Raspberry Pi
Affordable credit-card sized computer
Plugs into a computer monitor or TV
Uses standard keyboard and mouse
Can browse the internet and play HD video
Can also interact with the outside world!

## Slide 5: Models: Pi 4B
Broadcom BCM2711, Quad core Cortex-A72 (ARM v8) 64-bit SoC @ 1.5GHz
2GB, 4GB or 8GB LPDDR4-3200 SDRAM (depending on model)
2.4 GHz and 5.0 GHz IEEE 802.11ac wireless
Bluetooth 5.0, BLE Gigabit Ethernet
2 USB 3.0 ports; 2 USB 2.0 ports.
Raspberry Pi standard 40 pin GPIO header
2 × micro-HDMI ports (up to 4kp60 supported)
Vulkan 1.0 Micro-SD card slot
5V DC via USB-C connector
$40 - $100

## Slide 6: Models: Pi Zero 2 W
1GHz quad-core 64-bit Arm Cortex-A53 CPU
512MB SDRAM
2.4GHz 802.11 b/g/n wireless LAN
Bluetooth 4.2, Bluetooth Low Energy (BLE), onboard antenna
Mini HDMI port and micro USB On-The-Go (OTG) port
microSD card slot
CSI-2 camera connector
HAT-compatible 40-pin header footprint (unpopulated)
Micro USB power
65mm x 30mm
$10

## Slide 7: Models: Pi Pico
51 mm × 21 mm
Dual-core Arm Cortex-M0+ processor, flexible clock running up to 133 MHz
264KB on-chip SRAM
2MB on-board QSPI Flash
26 multifunction GPIO pins
1 × USB 1.1 controller
Micropython Programming Platform (Thonny)
Firmware
https://projects.raspberrypi.org/en/projects/getting-started-with-the-pico/

## Slide 8: How to setup a Raspberry Pi
You will need:
keyboard/mouse
HDMI, monitor
SD Card
Around 1 hour of time

## Slide 9: How to connect to sensors?
GPIO: General-Purpose Input/Output

## Slide 10: Raspberry PI Sensors
Flame sensor
Temperature and humidity
Moisture sensor
Water level sensor
Motion sensor
Collision sensor
Camera
Ultrasonic sensor
Sound sensor
…

## Slide 11: How to use these sensors?
DHT-22 as an example:
Reference: https://pimylifeup.com/raspberry-pi-humidity-sensor-dht22/
GPIO expansion board
Notes: resistance

## Slide 12: How to use these sensors?
DHT-22 as an example:
https://github.com/adafruit/Adafruit_Python_DHT
Install the library
Invoke the API:
output:
https://www.youtube.com/watch?v=IHTnU1T8ETk

## Slide 13: Arduino
Raspberry Pi ⇔ Arduino
Single Board Computing | Microcontroller development board
linux based OS | No OS
Multiple tasks | Single task
High level programming languages | C or C++
Built-in wireless modules | Addon wireless modules

## Slide 14: Arduino IDE
Connect Arduino Uno to your computer
Install and launch Arduino IDE
Create your project (open sample projects: Blink Arduino LED)
Select your arduino board in the IDE
Upload your program to the board
Run it!
Reference: https://www.techtonions.com/getting-familiar-with-arduino-ide/
Cross-compile: compiling code for one computer system on a different system

## Slide 15: Arduino + ROS
ROS (Robot Operating System)
1 /*
2 * rosserial Publisher Example
3 * Prints "hello world!"
4 */
5
6
7 //#define USE_USBCON
8
9 #include <ros.h>
10 #include <std_msgs/String.h>
11
12 ros::NodeHandle nh;
13
14 std_msgs::String str_msg;
15 ros::Publisher chatter("chatter", &str_msg);
16
17 char hello[13] = "hello world!";
18
19 void setup()
20 {
21 nh.initNode();
22 nh.advertise(chatter);
23 }
24
25 void loop()
26 {
27 str_msg.data = hello;
28 chatter.publish( &str_msg );
29 nh.spinOnce();
30 delay(1000);
31 }
http://wiki.ros.org/rosserial_arduino/Tutorials/Arduino%20IDE%20Setup

## Slide 16: ESP32
Hardware Updated Version of Arduino
Similar software (many Arduino applications can run on ESP32)
More built-in features (WiFi, BLE, sensors, WiFi mesh, Ethernet)

## Slide 17: Jetson TX2
OS: Linux (core: Ubuntu 18.04)
HW: GPU
First choice when you run deep learning tasks at the edge

## Slide 18: OS for IoT Devices
Linux: 38.7% for constrained devices, 54% for IoT Gateway
IoT OS: FreeRTOS, TinyOS, etc.

## Slide 19: FreeRTOS
Amazon FreeRTOS: open-source FreeRTOS kernel + libraries to securely connect devices to AWS cloud services.

## Slide 20: Sample Projects
Pedestrian Detection
https://create.arduino.cc/projecthub
Plastic Scanner
near-infrared spectroscopy

## Slide 21: Mobile Devices
Mobile Phones
Fitbit / Smart Watch
Smart Glasses
Other wearable devices?
Rings
Jacket

## Slide 22: Mobile Phones
Mobile phones in 2022 is more powerful than many servers in 2012
Higher CPU/GPU frequency (A15 Bionic system on a chip, 6 cores 3.2 GHz)
More memory (LPDDR4x) 6GB RAM (random access memory)
512GB SSD Storage
Higher network connectivity and speed
  NFC, BLE, WiFi, Low Earth Orbit Satellite Communication (Rumor)
  5G: 2Gbps
Limitation: battery powered

## Slide 23: Mobile Phones
Most Frequently Used Sensors:
GPS
Microphone
Cameras (front, rear)
WiFi/BLE
Accelerometer
Orientation sensor (Gyroscope)
Magnetic sensor
Light/Proximity
Screen

## Slide 24: Mobile Phone Sensors
GPS:
Receive signal from satellite (cannot be used in most indoor environments)
Accuracy: 30 cm to 10 meters (w/ and w/o ground station)
You don’t need to pay for its usage!

## Slide 25: Mobile Phone Sensors
Camera: 12 MP, with flashlight and lidar
Lidar: Light Detection and Ranging, depth information
Flashlight: heart rate detection
Lidar
Flashlight
Notes: Bump blood into the vessel

## Slide 26: Mobile Phone Sensors
Built-in Microphone and Speakers:
send/ hear sounds that we human cannot hear (20 - 20K Hz)
location differences in microphones can be used for object detection

## Slide 27: Mobile Phone Sensors
WiFi/BLE:
RSSI (received signal strength indicator)
  Related to distance between the receiver and the sender
  Related to the obstacles in the environment
BSS_ID, UU_ID
  BSS_ID: base station related
  UU_ID: application related

## Slide 28: Mobile Phone Sensors
Accelerometer: acceleration along three axes of the phone
Counting steps

## Slide 29: Mobile Phone Power Consumption
Video Recording > 3G WiFi Data Transmission > WiFi > GPS > Bluetooth
ZiFi: Wireless LAN discovery via ZigBee interference signatures (MOBICOM’10)

## Slide 30: Modular Phones
What is a modular phone? The phone can gain additional capabilities by changing different modules.
Project Ara (Google)
  CPU/Memory/display can all be exchangeable
Moto Z: backpack-like modules
  Speaker
  Better Camera
  Projector…
  Extra battery

## Slide 31: Smart Watches
Features:
Less powerful than a phone, but still pretty decent
WiFi/BLE, some with cellular/GPS module
Motion sensor (better way to capture your movements and gestures [CHI’16])

## Slide 32: Smart Glasses
Smart Glasses: Google Glasses, Lenovo ThinkReality A3 (released in 2021)
Gaming Device: Oculus

## Slide 33: Smart Glasses
Sensors
Eye cameras: capture user eye movement
Motion sensors
Microphone
Scene camera
Feedback:
Display
bone conduction speaker
Photo source: www.tobiipro.com

## Slide 34: 2023 will be the year of AR glasses ?
https://thenextweb.com/news/2023-year-ar-glasses-what-to-expect
Google, Meta, Apple, Microsoft (laid off recently-_-#)

## Slide 35: Vehicle as a mobile sensor
Vehicle Status Sensing
Environmental Sensing
Driver (passenger) Sensing

## Slide 37
Sensors:
LiDAR (128 beam)
Camera
Radar
Driving information:
Speed;
Location;
Vibration sensors
…
Driver Monitoring:
Camera
Smart wheel
https://medium.com/self-driven/how-fords-next-gen-test-vehicle-lays-the-foundation-for-our-self-driving-business-aadbf247b6ce

## Slide 38: Why so many sensors?
https://www.embedded.com/why-fir-sensing-technology-is-essential-for-achieving-fully-autonomous-vehicles/

## Slide 40: Outline
End Devices (data producers):
  Common features
  Raspberry Pi, Arduino, ESP32, Jetson TX2 NX
  mobile devices
  Vehicle as a mobile sensor
IoT Gateway
IoT Communication Protocols
  BLE, Zigbee
  MQTT, coAP, websocket
IoT applications:
  indoor localization
  smart home applications
  wireless sensor network

## Slide 41: Standard IoT Architectures
IoT nodes → Gateway → Cloud
Gateway: stationary plugged-in device
Other architectures? Infrastructureless (WiFi Direct)

## Slide 42: Smart Home Devices
Diverse devices

## Slide 43: Smart Home Devices
Smart Home Hubs: the brain of the smart home

## Slide 44: How do these hubs work?
Ideally: hubs providing computing and storage capabilities

## Slide 45: How do these hubs work?
Reality:
Echo is only a speaker and microphone with internet connection

## Slide 46: Smart Home Hubs Market Share
Your choice?

## Slide 47: Alexa Workflow
Device control logics can be processed either by AWS lambda functions or on device manufacturer’s cloud (3rd party cloud server).

## Slide 48: Let’s see an example:
How many senior detection methods given in the video? What are they? What are their limitations?
What is the method introduced in the video? Does it have any limitations?
Do you have any suggestions for future senior fall detection products?

## Slide 49: Outline
End Devices (data producers):
  Common features
  Raspberry Pi, Arduino, ESP32, Jetson TX2 NX
  smart home sensors and gateways
  mobile devices
IoT Gateway
IoT Communication Protocols:
  BLE, Zigbee, LoRA
  MQTT, coAP
IoT applications:
  indoor localization
  Personal sensing
  crowdsensing
  wireless sensor network

## Slide 50: IoT Communication Protocols
Physical Layer/Link Layer protocols (communication hardware)
  Zigbee
  Bluetooth Low Energy
  LoRA
Application Layer Protocols (communication software)
  MQTT
  coAP

## Slide 51: ZigBee
Varies network topology:
Used in industrial networks (WSNs)
Optimized for self-organized environments:
  Interference detection and channel switching
  Dynamic Rerouting
  Asymmetric link
Ad-hoc On-demand Distance Vector Routing
  What is distance vector?
  Why distance vector (not link state?)
Notes: Link Management: Each node maintains quality of links to neighbors. Link quality is used as link cost in routing
Asymmetric Link: Each node has different transmit power and sensitivity. Paths may be asymmetric.
Ad-hoc On-demand Distance Vector Routing ❑ On-demand ⇒ Reactive ⇒ Construct a route when needed ❑ Routing Table: Path is not stored. Only next hop. ⮚ Entry = <destination, next node, "sequence #" (timestamp)> ❑ Route Discovery: Flood a route request (RREQ) to all neighbors. Neighbors broadcast to their neighbors ❑ Request ID is the RREQ serial number. Used to discard duplicates. Source sequence # is a clock counter incremented when RREQ is sent. Destination sequence # is the most recent sequence from the destination that the source has seen. Zero if unknown

## Slide 52: Bluetooth
2.4-2.5 GHz ISM radio band, up to 3 Mbps
master / clients devices (piconet):
  master polls clients, grants requests for client transmissions
  parked mode: clients can “go to sleep” (park) and later wakeup (to preserve battery)
  Frequency hopping:
radius of
coverage
C
C
C
P
P
P
P
M
C
master device
client device
parked device (inactive)
P
M
Notes: Multi-access: polling…
Up to 7 active clients, 255 parket clients.

## Slide 53: Bluetooth Low Energy (BT4.x, 5.x)
40 Channels with 2MHz Spacing for Frequency hopping
3 channels reserved for advertising and 37 channels for data
Advertising channels specially selected to avoid WiFi interference
Two device types: peripherals and central
  Non-connectable advertising: Broadcast data
  Discoverable advertising: send data without connection (per request)
  Implementation: generic attribute profile (each attribute has a 16bit UUID)
Notes: Universally unique ID

## Slide 54: LoRa, the most popular LPWAN Tech
LoRa: Long Range…
9 miles
50 kbps
10 years

## Slide 55: Overview of LoRa
Multi-access Control: Pure Aloha
Notes: KPN (The Netherlands), which announced the previously mentioned nationwide LoRa network in The Netherlands end June,
Proximus (Belgium), the incumbent operator which was known as Belgacom previously and promises nationwide LoRaWAN coverage in the country by end 2016,
Orange (France), which started with 18 urban areas in the first quarter of 2016 and is expected to offer nationwide coverage soon as well,
Bouygues Telecom (France), also promising nationwide LoRa coverage by end 2016 and offering IoT services with its subsidiary company Objenious.
Unidata, an Italian telecom company, which announced the roll out of a LoRaWan network on June 14th. Initially this will be done in Rome with the promise of a full coverage of the city by 2017.
Netzikon, not a telecom firm but the name of a LoRaWan network which is present already in Stuttgart and will be rolled out nationwide in Germany by 2018 according to an October 4 press release by LPWAN provider Actility.

## Slide 56: IoT Protocols
MQTT: Message Queuing Telemetry Transport
  Publish, Subscribe (pub/sub)
  Lightweight (based on TCP)
https://www.reddit.com/r/COVID.RSS
Notes: tuh·leh·muh·tree

## Slide 57: MQTT - Topic
A topic forms the namespace
  Is hierarchical with each “sub topic” separated by a /
  myhome/floor/room/temp
A subscriber can subscribe to an absolute topic or can use wildcards:
    /Dearborn/TestRd/123/event
      Event in Apt 123, Test Rd, Dearborn
    /Dearborn/TestRd/+/event
      Events happens in all apts in TestRd in Dearborn
    /Dearborn/TestRd/123/#
      All information (event, alarm) in apt 123 TestRd, Dearborn

## Slide 58: Use on Constrained Networks
Protocol compressed into bit-wise headers and variable length fields.
  Potential privacy issue?

## Slide 59: Use on Constrained Networks
“Last will and testament” (LWT): reliability
Notes: MQTT IS BASED ON TCP

## Slide 60: Use on Constrained Networks
Provides multiple message delivery options

## Slide 61: MQTT for Request/Response
  Asynchronous bidirectional “push” delivery of messages to applications (no polling)
1) Client
- subscribe topic "function-xyz/response/<id>" //note: <id> is a client unique ID
2) Server
- subscribe topic "function-xyz/request/+" //note: "+" is a wildcard
3) Client
- publish topic "function-xyz/request/<id>" payload <input parameter>
4) Server
- receive notification "function-xyz/request/<id>" payload <input parameter>
- retrieve <id> from string
- process function-xyz(<input parameter>)
- publish topic "function-xyz/response/<id> " payload "<response>"
5) Client
- receive notification "function-xyz/response/<id>" payload "<response>"

## Slide 62: Try it for yourself?
Mosquitto： open source message broker that implements the MQTT protocol versions 5.
Test server:
2. Run mosquitto server on your own PC
Compared with http (on 3G network android)
  93x faster throughput
  11.89x less battery to send
  8x less network overhead
mosquitto_sub -h test.mosquitto.org -t "hello/world" –v
mosquitto_pub -h test.mosquitto.org -t "hello/world" -m "Who's there"

## Slide 63: CoAP
Constrained application protocol
  Lightweight HTTP (RESTful)
  UDP with reliability enhancement:
  Resource discovery

## Slide 64: Light-weight HTTP
Same:
  Request Methods: GET, POST, PUT, DELETE. (OBSERVE: subscribe to changes)
  Response Methods: 2.xx (success), 4.xx (client error), 5.xx (servererror).
  RESTful URI:
  e.g., coap://homegateway:port/sensor/light
  More information about RESTFUL: https://www.ibm.com/cloud/learn/rest-apis

## Slide 65: Light-weight HTTP
Different:
  Binary header:
    HTTP, text-based
  Request / Response share the same ID (like DNS)
  https://tools.ietf.org/html/rfc7252

## Slide 66: UDP-based
Message types:
  Request: Confirmable, Non Confirmable,
  Response: Acknowledgement and Reset
Example:

## Slide 67: UDP-based Reliability Enhancement
Confirmable Message Upon Message Lost:

## Slide 68: CoAP Resource Discovery
A well-known resource is used to discover other resources.

## Slide 69: Outline
End Devices (data producers):
  Common features
  Raspberry Pi, Arduino, ESP32, Jetson TX2 NX
  smart home sensors and gateways
  mobile devices
IoT Gateway
IoT Communication Protocols:
  BLE, Zigbee
  MQTT, coAP, websocket
IoT applications:
  indoor localization
  Personal sensing
  crowdsensing
  wireless sensor network

## Slide 70: Indoor Localization
GPS:
Works well in open area such as getting direction while driving
However, Fail or not work efficiently indoor area for instance inside large shopping mall due to obstacles
Solution: indoor positioning system

## Slide 71: WHAT IS INDOOR LOCALIZATION?
a process of tracking or detecting a object or a devices in the indoor environment using various technology and techniques such as Wi-Fi based Fingerprint approach (commonly used)

## Slide 72: Location-based Service (LBS)
Maps & Navigation:
Tracking Services:
Friends & family finder
Traffic (Museum)
Vehicle tracking
Information Services:
Local Search
Social networking
Context advertising
Gaming:
Layar

## Slide 73: Lots of Technologies
Wireless-based solution
Sensor-based solution
Multi-source fusion

## Slide 74: Wireless Signals for Localization

## Slide 75: What features of the wireless signal to use?
•Received Signal Strength Indicator (RSSI)
•Channel State Information (CSI)
•Fingerprinting/Scene Analysis
•Angle of Arrival (AoA)
•Time of Flight (ToF)
•Time Difference of Arrival (TDoA)
•Return Time of Flight (RToF)
•Phase of Arrival (PoA)

## Slide 76: Theoretical Foundation
Free Space Path Loss:
  Transmitter and receiver in free space
  Measured by: transmitted power – received power
Low accuracy in real environments
Notes: Second is the white space path loss model. White space means that there are no obstructing objects between the transmitter and the receiver. Pass loss can be measured by the difference between transmitted power at the sender and the received power at the receiver. What it says is that path loss is related to distance and radio signal frequency. Higher frequency level of the wireless radio and longer distances cause higher pass loss.
So when we want to improve the bandwidth of wireless communication, what we can do is to, first, raise the sending power. second, shorten the transmission distance, and then use a lower frequency. That’s one of the reason why wireless communication starts from using low frequencies. Like the original radio network, broadcast network, and voice phone network they all use frequencies lower than 1GHz. Now, the low frequency channels have been almost fully occupied. That’s why we move on to 5G. We communicate using higher frequencies so we can have wider radio channel ranges. To compensate the path loss, we deploy more cell towers to reduce the transmission distances.
One may wonder why cannot we increase the sending power. It is because our phones need to be senders as well and they are powered by batteries.

## Slide 77: Fingerprint
Offline training & Online matching

## Slide 78: Sensor Based IPS
Sensors:
Camera
  Surveillance
  Phone camera
  light-based
IMU (inertial measurement unit)
Odometry (robot)
Techniques:
Image processing
Dead reckoning

## Slide 79: Camera based indoor positioning
Mobile camera: heavy data collection and training
Surveillance camera: when applied in a public place with a lot of people
  What is one is blocked by others?
  Privacy issue
  How to associate user’s movement with their identity

## Slide 80: IMU based Positioning
Smart phone:
Quite accurate in counting steps
Not so good at detecting moving directions

## Slide 81: Indoor positioning systems
Joint usage of multiple technologies
Tradeoff between accuracy / deployment & Training cost
Some papers to read if you are interested:
Push the limit of WiFI based localization for smartphones
SpotFi: Decimeter level localization using WiFi

## Slide 82: My first research project

## Slide 83: Correction Points

## Slide 84: Experiment

## Slide 85: Result

## Slide 86: Personal Sensing
Activity recognition: aims to recognize the actions and goals of one or more agents from a series of observations on the agents' actions and the environmental conditions.
computer takes raw data as input and recognizes the user’s motion activity

## Slide 87: Activities
Simple activities: walking, sitting, standing, talking elevators…
Complex activities: shopping, smoking, driving, eating

## Slide 88: Process of activity recognition
Sensors:
Video sensors
  Fixed location
  May have privacy problem
Environmentmental sensors
  WiFi, Bluetooth, Infrared sensors
  Fixed location, limited inform
Wearable sensors:
  Equipped on human body
  Smart phones

## Slide 89: Data Collection
Start from scratch

## Slide 90: Applications
Recommended readings:
I am a Smartwatch and I can track my User’s Arm (gesture recognition)
Recognizing Smoking Gestures with Inertial Measurements Unit
Your Glasses Know Your Diet: Dietary Monitoring using Electromyography Sensors
Contactless Sleep Apnea Diagnosis on Smartphones(acoustic reflection)
E-eyes: Device-free Location-oriented Activity Identification Using Fine-grained WiFi Signatures
understanding and modeling of wifi signal based human activity recognition
Motion Tracking via Radio Reflections off the Body (WiTrack, see through the wall)
EQ-Radio: Emotion Recognition using Wireless Signals (vital signs)

## Slide 91: CrowdSensing
Crowdsensing, sometimes referred to as mobile crowdsensing, is a technique where a large group of individuals having mobile devices capable of sensing and computing (such as smartphones, tablet computers, wearables) collectively share data and extract information to measure, map, analyze, estimate or infer (predict) any processes of common interest. In short, this means crowdsourcing of sensor data from mobile devices.
Participatory sensing: individuals are actively involved in contributing sensor data
Opportunistic sensing: user involvement is minimal

## Slide 92: Crowd-Sensing for On-street Smart Parking
Objective: searching for free parking spots
1) infrastructure-based approaches; 2) users input

## Slide 93: Crowd Sensing based Traffic Detection
Apple/Google Map

## Slide 94: Wireless Sensor Network
Features:
  Sensors: battery-supported, sensing and communication (data relay)
  No backbone infrastructure or centralized control
  Sensitive to Energy Consumption/Latency/reliability
  Multi-hop self-organized mesh network:

## Slide 95: Building Monitoring / Intrusion Detection
Story about Shanghai Airport

## Slide 96: Zebranet
Purpose: track zebras on the field
Solution: GPS + Wireless Communication
ASPLOS'20 - ASPLOS Most Influential Paper Award https://www.youtube.com/watch?v=5c0IhQ07Hfo

## Slide 97: Delay Tolerant Network
Store, Carry, and Forward
  Usages: disaster response

## Slide 98: Basic Research Challenges:
Routing (Flooding) with Intermittent Connectivity

## Slide 99: What is IoT?
A network connecting (either wired or wireless) devices, or ‘things’, that is characterized by autonomous provisioning, management, and monitoring.
IoT is the next evolution of the Internet, connecting the unconnected people, processes, data, and things in your business today (Cisco)
IoT devices as those capable of two-way data transmission (excluding passive sensors and RFID tags). It includes connections using multiple communication methods such as cellular, short range and others. (GSMA)
Sensors & actuators connected by networks to computing systems. These systems can monitor or manage the health and actions of connected objects and machines. Connected sensors can also monitor the natural world, people, and animal” (McKinsey)

## Slide 100: What is IoT? (IEEE Internet of things journal)
“An IoT system is a network of networks where, typically, a massive number of objects, things, sensors or devices are connected through communications and information infrastructure to provide value-added services via intelligent data processing and management for different applications (e.g. smart cities, smart health, smart grid, smart home, smart transportation, and smart shopping).”

## Slide 101: If you are interested in IoT-related research
MobiSys, Sensys, MobiCOM
PerCOM
Ubicomp
https://www.youtube.com/watch?v=ULfg9MV4ymQ